## Slide 1: Daily Coffee Machine Cleaning routine
Classe 5 Model S 2 & 3 groupS

## Slide 2: Material
Blind filter
Portafilter
Cleaning brush
Cleaning powder
Sponge
Container
Steamer cleaning

## Slide 3
Replace the normal filter with the ‘’blind’’ filter (no holes)
Place 3gr (half a tea spoon) of the cleaning detergent in the portafilter
Cleaning Process

## Slide 4
Remove portafilter and rinse it with a bit of water
Place portafilter back into group head
Turn on coffee switch for 10 seconds then let it rest for 5 seconds
Repeat this step 10 times

## Slide 5
Turn on coffee switch for 10 seconds then let it rest for 5 seconds
Repeat this step 10 times
Use the brush to remove coffee oils and loose grinds from the group head

## Slide 6
Prepare the plastic container with hot water and 6gr (1 teaspoon) of cleaning detergent
Insert portafilters separated from the filters (with holes) into the plastic container and let it sit for 10-15 minutes
After the 10-15 minutes rinse everything under running water.
Use the yellow part of the sponge to remove coffee oils and loose grinds
Cleaning the Portafilters

## Slide 7
Reattach portafilter and lock the portafilter back into the group head
Remove cup holder grid and clean drain outlet.
Reattach cup holder grid

## Slide 8
Cleaning the steamer wand and milk frother
Follow the instructions in the back of the milk detergent

## Slide 9
Clean the machine with a damp cloth to remove stains
Finish with cleaning the outside