## Slide 1: Daily Coffee Machine Cleaning routine
RS1 Model & Invicta 2 & 3 groups

## Slide 2: Material
Blind filter
Portafilter
Cleaning brush
Cleaning powder
Sponge
Container
Steamer cleaning

## Slide 3
Replace the normal filter with the ‘’blind’’ filter (no holes)
Place 3gr (half a tea spoon) of the cleaning detergent in the portafilter
Automatic Cleaning Process

## Slide 4
Select the cleaning button from the screen display and select the group(s) to clean
Lock the portafilter into group head
Follow the on-screen instructions

## Slide 5
When the auto cleaning is finished, remove portafilter
Use the brush to remove coffee oils and loose grinds from the sides of the group head

## Slide 6
Prepare the plastic container with hot water and 6g (1 teaspoon) of cleaning detergent
Insert portafilters separated from the filters (with holes) into the plastic container and let it sit for 10-15 minutes
After the 10-15 minutes rinse everything under running water.
Use the yellow part of the sponge to remove coffee oils and loose grinds
Cleaning the Portafilters

## Slide 7
Reattach portafilter and lock the portafilter back into the group head
Remove cup holder grid and clean drain outlet
Reattach cup holder grid

## Slide 8
Cleaning the steamer wand and milk frother
Follow the instructions in the back of the milk detergent

## Slide 9
Clean the machine with a damp cloth to remove stains
Finish with cleaning the outside